## Slide 1
RTOS-Based Environmental Monitoring and Control System
C | FreeRTOS | STM32 | UART | I2C | GPIO
Gaurav Singh

## Slide 2
Project Overview
• Real-time embedded system for environmental sensor monitoring and control.
• FreeRTOS divides the application into independent tasks instead of one large polling loop.
• Core functions: sensor acquisition, data processing, UART communication, and fault monitoring.
• Designed for modularity, reliable inter-task communication, responsiveness, and maintainability.
2

## Slide 3
Project Objectives
• Acquire environmental sensor data periodically through STM32 peripheral interfaces.
• Use FreeRTOS tasks to separate sensing, processing, communication, and supervision.
• Exchange data safely between tasks using queues and protect shared resources using mutexes.
• Use UART for runtime monitoring and debugging.
• Handle time-sensitive events through interrupt-driven processing.
• Optimize task priorities, memory usage, and response time.
3

## Slide 4
Technology Stack
C
Embedded application logic
FreeRTOS
Scheduling, queues, mutexes
STM32
Microcontroller platform
I2C
Sensor communication
GPIO
Peripheral interface/control
UART
Serial output and debugging
4

## Slide 5
System Architecture
Environmental Sensors
Sensor Acquisition Task
Data Processing Task
UART Communication Task
Fault Monitoring Task
I2C / GPIO
Processed data
5

## Slide 6
FreeRTOS Task Design
• Sensor Acquisition Task — reads environmental sensors and places measurements into a queue.
• Data Processing Task — receives measurements and performs application-level processing.
• UART Communication Task — transmits measurements and diagnostic information to a serial terminal.
• Fault Monitoring Task — supervises abnormal system or sensor conditions.
• Task separation prevents slower communication or processing from directly blocking sensor acquisition.
6

## Slide 7
Inter-Task Communication & Synchronization
• FreeRTOS queues implement producer-consumer communication between acquisition and processing tasks.
• Queues buffer data and reduce direct dependency between tasks executing at different times.
• Mutexes protect shared resources when multiple tasks may access the same peripheral or shared state.
• Synchronization reduces race conditions and supports predictable real-time behavior.
7

## Slide 8
Interrupt Handling & UART Debugging
• Interrupt-driven event handling enables fast response to asynchronous hardware events.
• Interrupt Service Routines are kept short; heavier processing is deferred to normal FreeRTOS tasks.
• UART logs provide visibility into task execution, sensor acquisition, queue activity, and fault events.
• Runtime logs support troubleshooting and root-cause analysis during development.
8

## Slide 9
System Execution Flow
1
Initialize STM32 peripherals
2
Create queues and mutexes
3
Create FreeRTOS tasks
4
Start scheduler
5
Acquire sensor data
6
Process queued data
7
Transmit UART logs
8
Monitor faults / events
9

## Slide 10
Testing & Optimization
• Verify sensor acquisition, I2C/GPIO interfaces, queue transfer, UART communication, and fault handling.
• Use UART logs to observe execution and identify timing or communication problems.
• Tune task priorities to balance responsiveness and prevent starvation.
• Optimize stack sizes, queue capacity, and RTOS objects to control RAM usage.
• Keep ISRs concise and avoid unnecessary blocking to improve response time.
10

## Slide 11
Results & Engineering Outcomes
• Implemented a modular real-time architecture using independent FreeRTOS tasks.
• Used queues and mutexes for reliable task communication and shared-resource protection.
• Integrated UART, I2C, GPIO, and interrupt-driven event handling.
• Improved runtime reliability through debugging and optimization of task priorities, memory usage, and response behavior.
• Quantitative latency, CPU-load, RAM-use, and sensor-accuracy measurements were not provided, so they are not claimed here.
11

## Slide 12
Future Scope & Conclusion
• Future: add more sensors, configurable sampling, persistent logging, wireless/IoT connectivity, and watchdog-based recovery.
• Future: collect quantitative CPU load, task latency, stack usage, and sensor accuracy metrics.
• Conclusion: FreeRTOS provides a structured way to build a responsive and maintainable STM32 monitoring application.
• The project demonstrates practical embedded-system skills in RTOS scheduling, synchronization, peripheral interfaces, interrupts, and debugging.
12